EFILive Autocal Instructions 3.6.14

When you receive it:

Go to EFILive.com and download the latest version of the V8 and V7.5 software.

Open EFILive Scan and Tune (V8), and plug the autocal into your pc.  At the top of the page, there will be a "Check Firmware" Icon.  Click it.  Update the Bootblock and Firmware in the device.  In that order.

Next, connect the device to the car, turn to acc position, toggle through device and read the ECM File out, it will tell you to turn IGN off when it is done reading.  Turn key off and hit OK on the device.  It will save it on the device.

If its an auto, repeat process for T43 Trans module.

To email me those files, go to desktop and open EFILive Explorer.  On the bottom right, your tune files will be displayed that you just read.  Drag those to desktop or save in a folder if you like, and email them to me at ryan@gogwatney.com

Once they are saved on your pc, delete them from the device by right clicking and deleting the file.  This will keep available memory needed for datalogging.

Once I send updated files back, Open Efilive explorer and drag those files into the device.

Reboot the device, hook to car and upload the file(s) to the car.  Follow the prompts as you did when you read the file.

Now we can datalog.  With device connected, use the device to datalog.  I like to see a little idle time, normal driving and "spirited driving" all in the same log.  20-30 mins of datalog preferable.

Using EFilive explorer to retrieve the saved log, save and send to me from PC.  Delete it off the device.

We will repeat logging and updating tunes until we are spot on!